E2guardian mode	Implicit / Proxy	Transparent / Proxy	ICAP Server
Feature			Squid Implicit Proxy	Squid Trans Proxy
Site level filtering	yes	yes	yes	yes
URL level filtering	yes *	yes *	yes$	yes$
MITM to allow content filtering for https	yes	yes	yes$	yes$
App allow/block (via User-Agent header)	yes	http only	yes$	http only
Url redirection	yes *	yes *	yes$	yes$
Url modification (enforce safesearch etc)	yes *	yes *	yes$	yes$
Pass-through authentication ntlm, digest etc (requires upstream proxy)	yes	no	n/a	n/a
IP-based authentication (ident, IP-range, dns-auth, room based)	yes	yes	yes	yes
Proxy destination port based filter groups	yes	no	no	no
Squid-based user authentication	pass-through	no	yes	no
Username passed from Squid	no	no	yes	no
Upstream Proxy (e.g. Squid) optional	yes	yes	n/a	n/a
Content-checking	yes *	yes *	yes$	yes$
File type checking	yes *	yes *	yes$	yes$
Virus scanning	yes *	yes *	yes$	yes$
POST scanning	future*	future*	future$	future$
Single point of configuration	yes	yes	no	no

* MITM must be enabled for this feature to work with https. / $ Squid ssl-bump must be enabled for this feature to work with https.

2nd Draft for comments.